## Slide 1: Roaming Wars
How Different Devices Roam
- Jerry Olla -

## Slide 2: Previous related WLPC sessions
The Challenges of Modern Wi-Fi Roaming Including in 6 GHz | Wes Purvis
What Is New In iPhone Wi-Fi | Ben Toner

## Slide 3: Devices Tested
Apple M2 MacBook Pro (Wi-Fi 6E)
Apple iPhone 15 Pro (Wi-Fi 6E)
Windows 11 (24H2) Laptop
  Intel BE200 (Wi-Fi 7)
  Intel AX210 (Wi-Fi 6E) – Failed
  MediaTek MT7922 (Wi-Fi 6E)
  MediaTek MT7902 (Wi-Fi 6E)
  Qualcomm WCN7851 (Wi-Fi 7)
Android Pixel 8 (Wi-Fi 7)

## Slide 4: Drivers / OS
Windows 11 24H2 26100.2894
  Intel Driver: 11/11/2024 23.100.0.4 (BE200)
  MediaTek Driver: 6/11/2024 3.4.2.1046 (MT7902/MT7922)
  Qualcomm Driver: 12/1/2023 3.0.0.1078 (WCN7851)
iPhone 15 Pro
  iOS 18.3
M2 MacBook Pro
  macOS 15.2 (Sequoia)
Google Pixel 8
  Android 15
NOTE: All adapter/roaming options left at defaults

## Slide 5: Roaming Test – Manual Method
Aruba AP-735
(Wi-Fi 7)
Aruba AP-735
(Wi-Fi 7)

## Slide 6: Roaming Test - Automated Method
Automatically adjusted Tx power of each radio in +/- 1 dB increments every 3 seconds
RSSI levels balanced across bands – 2.4 GHz clamped to 6 dB less than 5/6 GHz
Devices in the same location and orientation for each test
60 min / 20 “power” cycles - per test
Captured 1000+ roaming events

## Slide 7: Roaming Test - Automated Method

## Slide 8: Do Tri-band devices Really prefer 6 GH?

## Slide 9: Tri-Band 2.4/5/6 GHz - 20/20/20 MHz Baseline – All things equal
Device | 2.4GHz | 5GHz | 6GHz | Roams
Google Pixel 8 (Wi-Fi 7) | 65% | 9% | 26% | 34
Intel BE200 (Wi-Fi 7) | 0% | 0% | 100% | 15
iPhone 15 Pro (Wi-Fi 6E) | 54% | 15% | 31% | 13
M2 MacBook Pro (Wi-Fi 6E) | 0% | 0% | 100% | 19
MediaTek MT7902 (Wi-Fi 6E) | 12% | 71% | 18% | 17
MediaTek MT7922 (Wi-Fi 6E) | 0% | 71% | 29% | 19
Qualcomm WCN7851 (Wi-Fi 7) | 0% | 68% | 32% | 19
Notes: No incentive other than band/frequency
Intel BE200 and MacBook Pro, they love 6 GHz

## Slide 10: Do Tri-band devices prefer wider channels?

## Slide 11
https://source.android.com/docs/core/connect/wifi-network-selection#candidate-scorers

## Slide 12
https://support.apple.com/guide/deployment/wi-fi-roaming-support-dep98f116c0f

## Slide 13: Tri-band 2.4/5/6 – 20/20/80 MHz Increase Ch. Width on 6 GHz to 80 MHz
Device | 2.4GHz | 5GHz | 6GHz | Roams
Google Pixel 8 (Wi-Fi 7) | 10% | 5% | 85% | 20
Intel BE200 (Wi-Fi 7) | 0% | 0% | 100% | 20
iPhone 15 Pro (Wi-Fi 6E) | 12% | 0% | 88% | 16
M2 MacBook Pro (Wi-Fi 6E) | 6% | 0% | 94% | 18
MediaTek MT7902 (Wi-Fi 6E) | 0% | 0% | 100% | 7
MediaTek MT7922 (Wi-Fi 6E) | 0% | 5% | 95% | 20
Qualcomm WCN7851 (Wi-Fi 7) | 5% | 30% | 65% | 20
Notes: All device love wider channels!

## Slide 14: Tri-Band 2.4/5/6 – 20/40/80 MHz Mixed Channel Widths
Device | 2.4GHz | 5GHz | 6GHz | Roams
Google Pixel 8 (Wi-Fi 7) | 0% | 0% | 100% | 24
Intel BE200 (Wi-Fi 7) | 0% | 0% | 100% | 19
iPhone 15 Pro (Wi-Fi 6E) | 46% | 15% | 38% | 13
M2 MacBook Pro (Wi-Fi 6E) | 0% | 0% | 100% | 19
MediaTek MT7902 (Wi-Fi 6E) | 29% | 0% | 71% | 7
MediaTek MT7922 (Wi-Fi 6E) | 0% | 0% | 100% | 20
Qualcomm WCN7851 (Wi-Fi 7) | 14% | 5% | 81% | 21

## Slide 15: Dual-band (5 & 6 GHz Only)
Notes: No 2.4 GHz

## Slide 16: Dual-Band 5/6 GHz - 40/80 MHz 5 + 6 GHz Only Test
Device | 2.4GHz | 5GHz | 6GHz | Roams
Google Pixel 8 (Wi-Fi 7) | 0% | 3% | 97% | 31
Intel BE200 (Wi-Fi 7) | 0% | 0% | 100% | 13
iPhone 15 Pro (Wi-Fi 6E) | 0% | 50% | 50% | 18
M2 MacBook Pro (Wi-Fi 6E) | 0% | 0% | 100% | 20
MediaTek MT7902 (Wi-Fi 6E) | 0% | 20% | 80% | 10
MediaTek MT7922 (Wi-Fi 6E) | 0% | 8% | 92% | 13
Qualcomm WCN7851 (Wi-Fi 7) | 0% | 61% | 39% | 18
Notes: Pretty much all clients prefer

## Slide 17: Does USING non-PSC Impact Roaming?

## Slide 18: Tri-band 2.4/5/6 – 20/40/40 MHz Non-PSC Test
Device | 2.4GHz | 5GHz | 6GHz | Roams
Google Pixel 8 (Wi-Fi 7) | 21% | 4% | 75% | 24
Intel BE200 (Wi-Fi 7) | 0% | 0% | 100% | 12
iPhone 15 Pro (Wi-Fi 6E) | 50% | 9% | 41% | 22
M2 MacBook Pro (Wi-Fi 6E) | 0% | 0% | 100% | 19
MediaTek MT7902 (Wi-Fi 6E) | 0% | 90% | 10% | 10
MediaTek MT7922 (Wi-Fi 6E) | 0% | 62% | 38% | 21
Qualcomm WCN7851 (Wi-Fi 7) | 0% | 36% | 64% | 22
Notes: Mediatek adapters struggle with Non-PSC channels

## Slide 19: Does 802.11k impact roaming?

## Slide 20: iOS & 802.11k
https://support.apple.com/guide/deployment/wi-fi-roaming-support-dep98f116c0f/web

## Slide 21: Tri-Band 2.4/5/6 – 20/40/80 MHz 802.11k enabled
Device | 2.4GHz | 5GHz | 6GHz | Roams
Google Pixel 8 (Wi-Fi 7) | 4% | 0% | 96% | 27
Intel BE200 (Wi-Fi 7) | 0% | 0% | 100% | 20
iPhone 15 Pro (Wi-Fi 6E) | 31% | 3% | 66% | 29
M2 MacBook Pro (Wi-Fi 6E) | 0% | 0% | 100% | 19
Mediatek MT7902 (Wi-Fi 6E) | 0% | 14% | 86% | 7
Mediatek MT7922 (Wi-Fi 6E) | 0% | 10% | 90% | 20
Qualcomm WCN7851 (Wi-Fi 7) | 10% | 25% | 65% | 20

## Slide 22: No 11k vs 11k enabled
Device | 2.4GHz | 5GHz | 6GHz | Roams | Test
Google Pixel 8 (Wi-Fi 7) | 0% | 0% | 100% | 24 | Tri-Band 20-40-80 MHz
Google Pixel 8 (Wi-Fi 7) | 4% | 0% | 96% | 27 | Tri-Band 20-40-80 MHz + 11k
Intel BE200 (Wi-Fi 7) | 0% | 0% | 100% | 19 | Tri-Band 20-40-80 MHz
Intel BE200 (Wi-Fi 7) | 0% | 0% | 100% | 20 | Tri-Band 20-40-80 MHz + 11k
iPhone 15 Pro (Wi-Fi 6E) | 46% | 15% | 38% | 13 | Tri-Band 20-40-80 MHz
iPhone 15 Pro (Wi-Fi 6E) | 31% | 3% | 66% | 29 | Tri-Band 20-40-80 MHz + 11k
M2 MacBook Pro (Wi-Fi 6E) | 0% | 0% | 100% | 19 | Tri-Band 20-40-80 MHz
M2 MacBook Pro (Wi-Fi 6E) | 0% | 0% | 100% | 19 | Tri-Band 20-40-80 MHz + 11k
MediaTek MT7902 (Wi-Fi 6E) | 29% | 0% | 71% | 7 | Tri-Band 20-40-80 MHz
MediaTek MT7902 (Wi-Fi 6E) | 0% | 14% | 86% | 7 | Tri-Band 20-40-80 MHz + 11k
MediaTek MT7922 (Wi-Fi 6E) | 0% | 0% | 100% | 20 | Tri-Band 20-40-80 MHz
MediaTek MT7922 (Wi-Fi 6E) | 0% | 10% | 90% | 20 | Tri-Band 20-40-80 MHz + 11k
Qualcomm WCN7851 (Wi-Fi 7) | 14% | 5% | 81% | 21 | Tri-Band 20-40-80 MHz
Qualcomm WCN7851 (Wi-Fi 7) | 10% | 25% | 65% | 20 | Tri-Band 20-40-80 MHz + 11k

## Slide 23: MLO and Roaming

## Slide 24: MLO Compatibility
Windows
Android

## Slide 25: Compare: No MLO vs MLO Enabled
Device | 2.4GHz | 5GHz | 6GHz | Roams | 
Google Pixel 8 (Wi-Fi 7) | 0% | 0% | 100% | 24 | 
Google Pixel 8 (Wi-Fi 7) | 19% | 38% | 44% | 16 | w/ MLO
Intel BE200 (Wi-Fi 7) | 0% | 0% | 100% | 19 | 
Intel BE200 (Wi-Fi 7) | 0% | 0% | 100% | 14 | w/ MLO
Qualcomm WCN7851 (Wi-Fi 7) | 14% | 5% | 81% | 21 | 
Qualcomm WCN7851 (Wi-Fi 7) | 14% | 14% | 71% | 14 | w/ MLO

## Slide 26: FILS Discovery (6 GHz Only)

## Slide 27: 6 GHz Only FILS Discovery Method
Device | 2.4GHz | 5GHz | 6GHz | Roams
Google Pixel 8 (Wi-Fi 7) | 0% | 0% | 100% | 2
Intel BE200 (Wi-Fi 7) | 0% | 0% | 100% | 8
iPhone 15 Pro (Wi-Fi 6E) | 0% | 0% | 100% | 7
M2 MacBook Pro (Wi-Fi 6E) | 0% | 0% | 100% | 18
Mediatek MT7902 (Wi-Fi 6E) | 0% | 0% | 100% | 4
Mediatek MT7922 (Wi-Fi 6E) | 0% | 0% | 100% | 19
Qualcomm WCN7851 (Wi-Fi 7) | 0% | 0% | 100% | 20

## Slide 28: 6 GHz Design Considerations
Optimize Tx power for 6 GHz
Design for secondary coverage
Use a wider channel on 6 GHz – Typically 80 MHz, if channel reuse allows
Use PSC channels when possible
Some AP vendors may not support using 40 MHz channels on PSC’s

## Slide 29: 6 GHz Design Considerations (Cont.)
Avoid mixing channel widths within the same band
Consider disabling some or all 2.4 GHz radios
Enable 802.11k, especially if supporting iOS devices
Some devices prefer 6 GHz more than others (Ex. MacBook & Intel BE200)
Avoid using 6 GHz only (FILS Discovery), use RNR by also enabling 5 GHz (or 2.4 GHz)

## Slide 30: Tools Used To Capture Roaming DATA

## Slide 31: iPhone/iPad
nOversight WiFi Analyzer
iOS app, available in app store
Live Wi-Fi analysis
Export roaming events to CSV file
https://www.numerousnetworks.co.uk

## Slide 32: macOS
nOversight Pro
Analyze Mac Roaming Behavior in detail
Record, Save, and Playback sessions
Analyze logs from iPhone/iPad
https://www.numerousnetworks.co.uk

## Slide 33: Windows
LSWIFI
CLI-centric Wi-Fi scanning tool for Windows
Live Wi-Fi connection analysis
Captures Wi-Fi roaming events
Log events to Remote Syslog Server
https://github.com/joshschmelzle/lswifi

## Slide 34: Android
Enable Developer Options and USB Debugging
Use adb (Android Debug Bridge)
Real-time Logging with adb logcat
  adb logcat -b all | grep -i wifi
Record Wi-Fi Roaming Events
  adb logcat -b all | grep -i "roam\|BSSID\|RSSI\|handover" > wifi_roaming_log.txt

## Slide 35: Wi-Fi 7 Capture Solution
Oscium Nomad – Wi-Fi Measurement Device
  4 Tri-band radios
  Wi-Fi 7 capable
Intuitibits Airtool 2 – macOS app for capturing Wi-Fi traffic using your Mac’s adapter
Capture Wi-Fi packets on up to 4 channels simultaneously
Save to PCAP or stream directly into Wireshark
https://oscium.com/
https://www.intuitibits.com
+
+
+

## Slide 36: Real-time Roaming Analysis
Ubiquiti WiFiman
Android & iOS
Live Roaming Analysis

## Slide 37: Demo

## Slide 38: Testing Results & slides
https://github.com/jolla/roaming-wars